## Slide 1
Lesson no 10
Tactical Data Links

## Slide 2
CONTENTS
01. Introduction to TDL
02. Link 11
03. Link 16
04. Link 22

## Slide 3
01. Introduction to TDL

## Slide 4
Tactical Data Links (TDLs) are a means to disseminate information processed from
        RADAR,
        SONAR,
        Identification Friend or Foe (IFF),
        Electronic Warfare,
        Self-Reporting
        Visual observation.

## Slide 6
Link 16 employs the Joint Tactical Information Distribution System (JTIDS) and Multifunctional Information Distribution System (MIDS) data link terminals.
Link 11 employs netted communication techniques and standard message formats for the exchange of digital information among airborne, land-based and shipboard tactical data systems.
Link 22 is a NATO secure radio system that provides Beyond Line-of-Sight (BLOS) communications. It interconnects air, surface, subsurface and ground-based tactical
data systems, and is used for the exchange of tactical data among the military units
of the participating nations.

## Slide 7
The Situation Awareness Data Link (SADL) is an air-ground EPLRS application used by both the US Air Force and US Army as an anti-fratricide measure. Fully integrated into Close Air Support (CAS) aircraft, SADL can be used in three types of networks:
- Air-to-Air – for airspace SA
- Air-to-Ground – for interoperability with EPLRS-equipped units
- Gateway – two-way exchange of SADL and Link 16 SA/Command and Control (C2)
The Enhanced Position Location Reporting System (EPLRS) is a high capacity TDL that can provide simultaneous voice, data and situation awareness (SA). It is a self forming, self healing mesh network that automatically relays from one radio to another.
The Multifunctional Advanced Data Link (MADL) is a high data rate, K-band communication link with LPI and LPD characteristics. The objective of MADL is to provide an airborne data link that supports cooperative engagements between stealth
aircraft without compromising stealth observability performance.

## Slide 8
02. Link 11

## Slide 9
Link 11 employs netted communication techniques and standard message formats for the exchange of digital information among airborne, land-based, and shipboard tactical data systems.
Providing mutual exchange of information among net participants using highfrequency (HF) or ultrahigh-frequency (UHF) radios, Link 11 is a half-duplex, netted, secure data link.
Link 11 requires a Net Control Station (NCS) and Participating Units (PUs) to operate.

## Slide 10
A representative Link 11 system configuration, consists of
          - a computer system,
          - an encryption device,
          - a data terminal set (DTS),
          - an HF or UHF radio,
          - a coupler,
          and an antenna.
The computer system is called a Tactical Data System, or TDS. Airborne units are referred to as Airborne TDSs, or ATDSs, and shipboard units are referred to as Naval Tactical Data System, or NTDSs.
The encryption device, or crypto, is a Key Generator-40 Alpha (KG-40A).

## Slide 13
03. Link 16

## Slide 14
Link 16 is a
    - frequency-hopping,
    - jam-resistant,
    - high-capacity data link.
Operating on the principle of Time Division Multiple Access (TDMA), wherein 128 time slots per second are allocated among participating JTIDS Units (JUs),
time slots are organized into multiple functional Network Participation Groups (NPGs).

## Slide 15
Link 16 enhances tactical employment of all equipped platforms and provides certain technical and operational improvements to existing tactical data link capabilities, which include:
    - Nodelessness
    - Jam resistance
    - Improved security
    - Increased data rate (throughput)
    - Increased volume and granularity of information exchange
    - Reduced data terminal size, allowing installation in fighter and attack aircraft
    - Digitized, jam-resistant, secure voice capability
    - Relative navigation
    - Precise Participant Location and Identification (PPLI)

## Slide 16
The acronym “JTIDS” refers to the Joint Tactical Information Distribution System, the first-generation Link 16 terminal.
The Multifunctional Information Distribution System (MIDS) Low-Volume Terminal (LVT) is the second generation of Link 16 terminals.
The next generation of Link 16-capable radios will be the Joint Tactical Radio System (JTRS) and MIDS JTRS.

## Slide 18
03. Link 22

## Slide 19
The Link 22 goals are to replace Link 11,
    - thereby removing the inherent limitations of Link 11;
    - to improve Allied interoperability; to complement Link 16;
    - and to enhance the commanders’ war fighting capability.

## Slide 22
Thanks